Govt. Women Engineering College, Ajmer

All the Best			Department of Computer Science and Engineering                                 A

B. Tech V Semester I Mid Term Examination – September 2017

Subject:  CA 	 Subject Code: 5CS1		Time: 1 Hr.	 Max. Marks: 20	Date of Examination: 18/09/2017

------------------------------------------------------------------------------------------------------------------------------------------------------------------------------

Q. 1 Discuss, RISC vs. CISC											[5]

Q. 2 A non pipelined single cycle processor operating at 100 MHZ is converted into a synchronous pipelined processor with five stages requiring 2.5 nsec, 1.5 nsec, 2 nsec, 1.5 nsec and 2.5 nsec respectively. The delay of latches (buffer between two stages) is 0.5 nsec. The speedup of pipelined processor for a large number of instructions is. 											[3]

Q. 3 Discuss Shift Micro Operations with diagram and example. 				 		[3]

Q. 4 Draw the block diagram of the hardware that implements the following statement.

xyT0 + T1 + y’T2 : AR    AR + BR  					         [4]

Q. 5 Construct a common bus system by Three-state buffer gate for 4 Register each of which having 4 bits.

And consider a common bus constructed by multiplexer for 16 registers of 32 bit each. Then, how

many multiplexer are required and what is the size of each multiplex. 					[5]

Govt. Women Engineering College, Ajmer

All the Best			Department of Computer Science and Engineering                                 B

B. Tech V Semester I Mid Term Examination – September 2017

Subject:  CA 	 Subject Code: 5CS1		Time: 1 Hr.	 Max. Marks: 20	Date of Examination: 18/09/2017

------------------------------------------------------------------------------------------------------------------------------------------------------------------------------

Q. 1 Show that the theoretical maximum speedup that a pipeline can provide is equal to the number of

segments in the pipeline. 										[5]

Q. 2 Illustrate the influence of the number of addresses on computer program for the arithmetic expression

X = (A+B) x (C+D) using Zero, One, Two and Three Address instruction with the advantages and

disadvantages of each.											[5]

Q. 3 Design a 4-bit combinational circuit of decrementer by using four full-adder circuits        		[3]

Q. 4 Explain the Register Transfer of Fetch and Decode phase in Instruction Cycle with respect to timing

signals. 													[4]

Q. 5 Discuss the Flynn Classifications 							                        [3]

Govt. Women Engineering College, Ajmer

All the Best			Department of Computer Science and Engineering                                 C

B. Tech V Semester I Mid Term Examination – September 2017

Subject:  CA 	 Subject Code: 5CS1		Time: 1 Hr.	 Max. Marks: 20	Date of Examination: 18/09/2017

------------------------------------------------------------------------------------------------------------------------------------------------------------------------------

Q. 1 Discuss the instruction pipeline for the instruction cycle that is divided into four segments of equal

duration with handling of branch type instructions.							[5]

Q. 2 Explain Addressing Modes in details with suitable example and diagrams.				[5]

Q. 3 Draw the block diagram of Common bus of 4 Registers of 8 bit each.					[4]

Q. 4 Show the block diagram of the hardware that implements the following register transfer statement.

If (P=1) then  (R1     R2) else if (Q=1) then (R1    R3) 							[4]

Q. 5 Discuss the Von-Neumann 			 							[2]