Roll No………………. Total no. of pages: 1 Model Paper (Mid Term) B.Tech. I Sem.2018-19 (CSE Section B) Engineering Chemistry Topic: Water & Water Treatment and Fuel

Time: 1 hr.								Maximum marks: 16

Instruction to Candidates:

Attempt all questions. Schematic diagrams must be shown wherever necessary. Any data you feel missing suitably be assumed and stated clearly. Units of quantities used/ calculated must be stated clearly. Word Limit for Part-A 10-20 words, for Part-B 25-50, Part-C long answer type/ 100 or more than 100 words

PART -A

Q.1 Define hardness of water. Give formula of any one chemical responsible for temporary hardness.										         [1]

Q.2 What is carbonization?								         [1]

PART -B

Q.3 What is priming in boiler water. Give main causes of priming.			         [2]

Q.4 Differentiate between HCV & LCV. 						         [2]

Q.5 Write short note on Boiler Corrosion.					                     [3]

Q.6 Give main differences between Cold & Hot Lime Soda Process.	                     [3]

PART -C

Q.7 A water sample has the analytical report as under (in ppm):

Mg(HCO3)2 =73, Ca(HCO3)2 =81, CaCl2 = 55.5, Mg(NO3)2 = 37, KCl = 20. Calculate the amount of lime (85%pure)  and Soda(80%pure) for softening of 80,000 litre of water.     [4]

OR

Q.7 A sample of coal was found to contain the following % composition by weight:

C= 75%, H= 5.2%, O = 12.1%, N = 3.2%, ash = 4.5%. Calculate GCV and NCV using Dulong’s Formula.  									         [4]

……………………………………………………………………………………………….

ANSWERS

PART -A

Ans.1 Hardness of water is the property of water to prevent the lathering of soap. In other words it is termed as “soap consuming capacity”. Chemical responsible for temporary hardness is Ca(HCO3)2.

Ans.2 The conversion of coal into coke is known as carbonization. It is also known as destructive distillation.

PART -B

Ans.3 When a boiler is producing steam very rapidly some particles of the water carried along with the steam. This process of ‘WetSteam’ formation is called priming.

It is caused by:

- Presence of large amount of dissolved solids such as alkali sulphate and chlorides

- Sudden boiling

- Improper boiler design

- Sudden increase in steam-production rate

Ans.4 Higher Calorific Value (HCV): The total amount of heat liberated when unit mass or unit volume of the fuel has been burnt completely and the products of combustion are condensed at room temperature.

Lower Calorific Value (LCV): The total amount of heat liberated when unit mass or unit volume of the fuel has been burnt completely and the products of combustion are allowed to escape.

Ans.5 Destructive attack or decay of boiler material or metal by chemical or electrochemical reaction with its environment. The most common source for boiler corrosion is dissolved gases viz. oxygen, carbon dioxide, ammonia and acidic contaminants. The brief description on boiler corrosion is as follows:

Water usually contains about 8ml D.O/L at room temperature. D.O. in water and presence of high temperature attacks boiler material

2Fe   +   2H2O +   O2    →     2Fe (OH)2↓

4Fe(OH)2↓ + O2            →    2[Fe2O3.2H2O]

Ferrous hydroxide                       (Rust)

Removal of Dissolved Oxygen

- Chemically, oxygen is removed by adding oxygen scavenger or absorbing chemicals in a calculated amount such as sodium sulphite or hydrazine or sodium sulphide.

- Hydrazine is used in large utility boiler store move dissolved oxygen but not recommended for heating boilers because it must be closely controlled because of explosive nature of hydrazine and if used excess, it decomposes to produce ammonia which again cause corrosion.

Ans: 6

| S.N. | Cold L-S Process | Hot L-S Process |
| --- | --- | --- |
| 1. | Process carried out at room temperature | Process carried out at high temperature |
| 2. | Reactions are slow | Reactions are fast |
| 3. | Softening Capacity is low. | Softening Capacity is high. |
| 4. | Coagulants are used for removal of fine particles. | No requirement of coagulants. |
| 5. | Requirement of lime is as per stoichiometry. | Lesser amount of lime is required because temporary hardness, CO2, H2S are removed at elevated temperature. |
| 6. | Steam is not used. | Steam is used hence there is fuel consumption. |
| 7. | Residual hardness of water after treatment is 50-60 ppm. | Residual hardness of water after treatment is 15-30 ppm. |

PART -C

Ans.7 First conversion into CaCO3 equivalent:

| Constituents | Amt. (ppm) | in CaCO3 eq. | Chemical Reactions | Requirement (L/S) |
| --- | --- | --- | --- | --- |
| Mg(HCO3)2 | 73 | 73*100/146=50 | Mg(HCO3)2 + 2Ca(OH)2 ( Mg(OH)2 + 2 CaCO3 + 2H2O | 2L |
| Ca(HCO3)2 | 81 | 81*100/162=50 | Ca(HCO3)2 + Ca(OH)2 ( 2 CaCO3 + 2H2O | L |
| CaCl2 | 55.5 | 55.5*100/111=50 | CaCl2 + Na2CO3 ( CaCO3 + 2NaCl | S |
| Mg(NO3)2 | 37 | 37*100/148=25 | Mg(NO3)2 + Ca(OH)2 ( Mg(OH)2 + Ca(NO3)2 Ca(NO3)2 + Na2CO3 ( CaCO3 + 2NaNO3 | L+S |
| KCl | 20 | Doesn’t cause hardness | -- | -- |

Amount of lime required = 74/100 [2 x Mg(HCO3)2 +  Ca(HCO3)2 + Mg(NO3)2 all in terms of CaCO3 equivalent] x volume of water x purity factor

Amount of lime required = 74/100 [2x 50 +50 + 25] x 80000 x 100/85 = 12188235.29mg =12.19 Kg

Amount of soda required = 106/100 [CaCl2 + Mg(NO3)2 all in terms of CaCO3 equivalent] x volume of water x purity factor

Amount of soda required = 106/100 [50+25] x 80000 x 100/80 = 7950000mg= 7.95 Kg

OR

Ans.7 According to Dulong’s Formula:

GCV = 1/100 [ 8080 C + 34500(H-O/8) + 2240S] Cal/g.

GCV = 1/100 [ 8080 x 75 + 34500 (5.2 – 3/8) + 2240 x 2]

GCV = 1/100 [606000 + 166462.50 + 4480] = 7769.425 Cal/g

NCV = (GCV – 0.09 H x 587) Cal/g.

NCV = (7769.425 – 0.09 x 5.2 x 587) = 7494.709 Cal/g

……………………………………………………………………………………….