Roll No………………. Total no. of pages: 1 Model Paper (Mid Term) B.Tech. I Sem.2018-19 (CSE Section B) Basic Mechanical Engineering Topic: Refrigeration/Air Conditioning/Engg.Materials & heat treatment of steel

Time: 1 hr.								Maximum marks: 16

Instruction to Candidates:

Attempt all questions. Schematic diagrams must be shown wherever necessary. Any data you feel missing suitably be assumed and stated clearly. Units of quantities used/ calculated must be stated clearly. Word Limit for Part-A 10-20 words, for Part-B 25-50, Part-C long answer type/ 100 or more than 100 words

PART -A

Q.1 Define Creep.									         [1]

Q.2 Define Refrigeration.								         [1]

PART -B

Q.3 Differentiate between Thermoplastic and Thermosetting Materials.		         [2]

Q.4 Name the major types of refrigeration system. Which refrigeration system is used in domestic refrigerator   						                                 [2]

Q.5 Write a short note on classification of ferrous materials				         [3]

Q.6 What is the Coefficient of performance? What is its significance? 	                     [3]

PART -C

Q.7 What are the major components of Window air conditioning? A refrigerator plant is of one ton capacity. It is driven by a motor of 0.5 kW. Find the COP of refrigerator considering 95% capacity.    								        [4]

ANSWERS

PART -A

Ans.1 Creep is a time-dependent deformation of a material while under an applied load that is below its yield strength.

Ans.2 Refrigeration can be defined as the process of transferring heat from low temperature region to a higher temperature region.

PART -B

Ans.3

| Thermoplastic Materials | Thermosetting Materials |
| --- | --- |
| The polymers whose shape can be changed on application of heat and pressure are known as thermoplastics. | The polymers which after making resist strongly to any alteration of its shape by application of heat and pressure. |
| Thermoplastics have weak forces of interaction among the chains. | The whole mass of polymer is well connected with strong forces of interaction among the chains. |

Ans.4 (a) Vapour Absorption Refrigeration System

(b) Vapour Compression Refrigeration System

The working of Domestic Refrigerator based on Vapour Compression Refrigeration System

Ans.4 Ferrous Materials:

- These are the metals and alloys containing a high proportion of the element iron.

- They are the strongest materials available and are used for applications where strength is required at relatively low cost and where weight is not of primary importance.

- These ferrous materials are used in bridge buildings and railway lines etc.

These ferrous materials can be classified in different families as shown below:

Ans: 6  Ratio of work or useful output to the amount of work or energy input, used generally as a measure of the energy-efficiency of air conditioners, space heaters and other cooling and heating devices

PART -C

Ans.7 The major components of Window Air Conditioner are:

- Evaporator (ii) Condenser (iii) Compressor (iv) Air Filters (v) Fans

COP = Q/W

Q = 1 ton = 210KJ/min., W = 0.5 KW = 0.5/0.0167 KJ/min.

COP = 210 KJ/min x 0.0167/ 0.5 x 95/100  = 6.65

……………………………………………………………………………………….